T-REX Real-Time Model Information

Organization:	U.S. Army Research Laboratory & Army High Performance

Computing Research Center (AHPCRC)

Numerical Model:	WRF-ARW

Points of Contact:	Robert Dumais

Army Research Laboratory

CISD/BE

WSMR, NM, 88002-5501

rdumais@arl.army.mil

(505) 678-4650

Edward Colon

Army High Performance Computing Research Center

Army Research Laboratory

CISD/BE

Adelphi, MD  20783

ecolon@arl.army.mil

(301) 394-1875

Horizontal Resolution:  2 km (finest mesh displayed on EOL website)

Number of Grids: 3

Horizontal Grid Size(s): 18 km (91x91), 6 km (133x133), 2 km (157x157)

Vertical Levels: 40 eta levels with model top of 10 mb

Initial Conditions:  NCEP’s 06Z UTC GFS cycle

Data Assimilation:	None

Lateral Boundaries:	NCEP’s 06Z UTC GFS cycle

Forecast Length:	48 hours, initialized at 12z daily

Physics:

- Lin microphysics

- Kain-Fritsch Eta CPS (18 & 6 km mesh only)

- w-damping turned on

- 3:1 grid space (km)- to- time step (s) ratio

- Dudhia short wave radiation (called every 10 min)

- NOAA land surface model

- YSU PBL & surface similarity

- conventional terrain averaging

- Runge-Kutte 3rd order dynamics

- two-way nest feedback

- diffusion damping method (Klemp & Lilly, 1978)

- dampcoef=0.01 & zdamp set to 5000m

- divergence damping (0.1) & external mode damping (0.01)

- diff_opt=1 (2nd order diffusion on coordinate surfaces)

- km_opt=4 (horizontal Smagorinsky 1st order closure)

- 5th order horizontal advection of momentum & scalars

- 3rd order vertical advection of momentum and scalars

Output Format: NetCDF; GRADS-generated gif files