9/01/2012

Aircraft Research Instrumentation

GV - Basic RAF DC3 Configuration

Cantrel et al

RAF-Supplied Instrumentation:

I.  Airborne Data System.

A. Acquisition.  GV ADS3.

NCAR Distributed Sampling Modules (9 units), one in

each of 6 wing pylons, 1 in radome, and 2 in the cabin.

B. Cabin Displays(3):

Dell Latitude Pentium MMX-266 Laptops (2)

Mission Coordinator Station

II. Aircraft Position, Velocity and Attitude

A. Honeywell Laseref IV SM Inertial Reference Systems (2).

(Name, Name_IRS2).

B. Garmin GPS16 Global Positioning System. (GGName_GMN).

C. NovAtel Model OEM 4 L1/L2 Differential GPS High Accuracy

Positioning System (GGName)

D. Avionics GPS (Name_G)

III. Static Pressures.

A. Paroscientific Model 1000 Digital Pressure Transducer -

Fuselage Port (PSF).

B. Avionics Sensor - Corrected (PS_A).

IV. Dynamic Pressures.

A. Honeywell PPT (0-5 PSI) Absolute Pressure Transducer – Radome

(QCR).

B. Honeywell PPT (0-5 PSI) Absolute Pressure Transducer  – Nose

Cone Pitot (QCF).

C. Honeywell PPT (0-5 PSI) Absolute Pressure Transducer – Wing

Gust Pod(QC_GP).

D. Avionics Sensor – Corrected (QC_A).

V.  Temperatures.

A. Rosemount Type 102 Sensor -- Rosemount Model

510BF Amplifier - Port Fuselage Mount (TTRL)).

B. HARCO De-iced Dual Temperature Sensor – Starboard Fuselage

Mount (TTHR1, TTHR2).

C. Avionics Heated Rosemount Temperature Sensor – Port Fuselage

Mount (TT_A, AT_A).

VI. Flow Angle Sensors, Radome.

A. Attack – Honeywell PPT (+- 1 PSI) Differential Pressure

Transducer (ADIFR).

B. Sideslip – Honeywell PPT (+- 1 PSI) Differential

Pressure Transducer (BDIFR).

GV RAF DC3

Page 2

VII. Dew Point and Humidity.

A. Buck Research, Model 1011C Dew Point Hygrometer –

Port Fuselage Mount (DP_DPL).

B. Buck Research, Model 1011C Dew Point Hygrometer - 	    	   	   	   Starboard Fuselage Mount (DP_DPR).

C. VCSEL TDL Hygrometer – Fuselage Aperture (DP_VXL).

VIII. Special Request Equipment

- CARI – Picarro CO2/CH4 Analyser.  Std HIMIL Inlet

- CARI – Carbon Monoxide Analyzer.  Std HIMIL Inlet

- CARI – NO/NO2 Analyzer.  Std HIMIL Inlet

- CARI - Fast Ozone Analyzer.  Std HIMIL Inlet.

- RAF CN Counter.  HIMIL Inlet

- ACD/EOL SMPS Aerosol Particle Sizer. HIMIL Inlet

- HAIS TOGA Analyzer.  Special Chemistry HIMIL Inlet.

- HAIS GT-CIMS.  Special Chemistry HIMIL Inlet.

- HAIS HARP Irradiance / Actinic Flux Suite

IX. Wing Stores

- All Weather Wing Gust Pod. Wing Position – RWOO

- RAF – DMT Cloud Droplet Probe

Size Distribution, 3 – 45 um. Wing Position - LWII

C.   RAF – Modified PMS 2D-C Optical array Probe

Size Distribution, 25 to 1600 um. Wing Position - LWIO

D.   RAF – DMT UHSAS Aerosol Probe.  Wing Position - LWOI

Size Distribution, 60 – 1000 nm.

E.   Cloud Particle Imager (3V-CPI). Wing Position - RWI

Detection size, 25 um and greater.

- Rosemount Icing Rate Indicator (RICE). Wing Position – LWI

- CU Total Water Sensor. Wing Position - LWOO

X. Photography

A.   Point Grey Model Flea Digital Video Camera.  Forward facing

in wing pylon. (1 sec images recorded).

- Point Grey Model Flea Digital Video Camera. Starboard facing.

- sec images recorded).

- Point Grey Model Flea Digital Video Camera.  Port facing.

(1 sec images recorded).

XI. User Supplied Instruments

- USNA P-CIMS Peroxides Analyzer. Special Chemistry HIMIL Inlet

- CU Formaldehyde Analyzer (H2CO, HCOOH). Special Chemistry

HIMIL Inlet