Summary of Calibration Factors

C-130 - Basic PLOWS Configuration

Rauber et al

Pre-Calibration – 10/23/09

Param

Variable                    Name      C1        C2       C3

Dynamic Pressure-Fuselage L. (hPa)	QCF  	   0.919	  17.257  -.0073

Dynamic Pressure-Radome (hPa)	QCR 	  -1.418	  17.254	-.0018

Dynamic Pressure-Fuselage R. (hPa)	QCFR	  -0.456	  13.772  -.0018

Total Temperature-Radome Right (oC)	TTRR	 -68.309	  27.092	-.4413

Total Temperature:Heated- Wing (oC)  TTWH    -68.225    28.126  -.4160

Remote Surface Temp. Bot. (oC) 	RSTB    -47.098     8.434   .1757

Remote Surface Temp.-Bot. (oC) 	RSTB1   -53.531    10.405   .0201

Remote Surface Temp. Top. (oC)	RSTT    -55.600    11.723  -.0960

Vertical Press. Diff. Radome(mb)	ADIFR	  -0.846     6.942	 .0028

Horizontal Press. Diff. Radome(mb) 	BDIFR	  -0.099     5.137   .0008

Cabin Pressure (hPa)                 PCAB     -1.194   108.496  -.0272

CN Inlet Pressure (hPa)              PCN       7.254   106.036  -.0205

CN Flow Rate (slpm)	FCN	   0.000	   0.323   .0000

Dew Point Sensor Bottom (C)	DPB	  -1.5       1.0     .0

Dew Point Sensor Top (C)	DPT	  -1.8       1.0     .0

Post Calibration – 12/01/08

Param

Variable                    Name      C1        C2       C3__

Dynamic Pressure-Fuselage L. (hPa)	QCF#  	   0.866	  17.220   .0002

Dynamic Pressure-Radome (hPa)	QCR# 	  -1.211	  17.098	 .0508

Dynamic Pressure-Fuselage R. (hPa)	QCFR#	   0.155    13.660   .0107

Total Temperature-Radome Right (oC)	TTRR	 -64.245	  27.044	-.4363

Total Temperature: Heated- Wing(oC)  TTWH#   -67.738    28.169  -.4114

Remote Surface Temp. Bot. (oC) 	RSTB    -53.285     9.875   .0431

Remote Surface Temp.-Bot. (oC) 	RSTB1   -50.332     9.189   .0894

Remote Surface Temp. Top. (oC)	RSTT    -52.354     9.909   .0486

Vertical Press. Diff. Radome(mb)	ADIFR	   0.245     6.933	 .0028

Horizontal Press. Diff. Radome(mb) 	BDIFR	   0.241     5.145  -.0004

Cabin Pressure (hPa)                 PCAB     -3.185   108.940  -.0585

CN Inlet Pressure (hPa)              PCN      -5.642   109.130  -.0359

Dew Point Sensor Bottom (C)	DPB	  -0.400     1.035   .0018

Dew Point Sensor Top (C)	DPT	  -0.597     1.059   .0038

# Post cal used in final processing.

Calibration Summary

page 2

Calibration Maneuvers –

RAF uses sets of in-flight maneuvers specifically designed to help evaluate the performance of the 3-D wind measurement system on the aircraft.  Sets of maneuvers were flown on one test flight and two research flights: TF01, RF08 and RF13 respectively. In each case the variations observed fell within acceptable limits.

PMS - 1-D Probe Bin Sizes

The SPP100 (std), SPP100 (modified) and CDP probes were used on the project.  The minimum droplet size (microns) for each sampling bin are listed below:

SPP100		 SPP100

Std  		  Mod             CDP

bin#1 		 3.5   um		 4.25  um		  1.875 um

bin#2		 	 4.815		 5.32		  2.91

bin#3			 6.13 		 6.39		  3.94

bin#4			 7.445		 7.46		  4.98

bin#5			 8.76		 8.53		  6.01

bin#6			10.075		 9.60		  7.045

bin#7			11.39		10.67		  8.08

bin#8			12.705		11.75		  9.11

bin#9			14.02		13.685		 10.15

bin#10		15.335		15.62		 11.18

bin#11		16.65 		17.555		 12.215

bin#12		17.965		19.49		 13.25

bin#13		19.28		21.425		 15.29

bin#14		20.595		23.36		 17.33

bin#15		21.91		25.295		 19.37

bin#16		23.225		27.23	  	 21.41

bin#17		24.54		29.165		 23.45

bin#18		25.855 		31.10	  	 25.49

bin#19		27.17		33.035		 27.53

bin#20		28.485		34.97		 29.57

bin#21		29.80		36.905		 31.61

bin#22		31.115		38.84		 33.65

bin#23		32.43		40.775		 35.69

bin#24		33.745		42.71		 37.73

bin#25		35.06		44.645		 39.77

bin#26		36.375		46.58		 41.81

bin#27		37.69		48.515		 43.85

bin#28		39.005		50.45		 45.89

bin#29		40.32		52.385		 47.93

bin#30		41.635		54.32		 49.97

bin#31		42.95		56.25		 52.01