Table of Contents

Chapter 7.  Sounding Operations	1

7.1	Driftsonde Facility	1

7.2	Ground-based Radiosonde Stations	1

7.2.1  Russia	2

7.2.2  Democratic People's Republic of Korea (North Korea)	4

7.2.3  Republic of Korea (South Korea)	5

7.2.3.1 Enhanced Observations as Part of the Korean Enhanced Observing Period (KEOP)	6

7.2.4  Japan	6

7.2.4.1 Enhanced Observations as Part of Typhoon Hunter-2008 (TH-08)	8

7.2.5  China	8

7.2.6  Micronesia, Brunei and Guam	11

7.2.6.1  PALAU2008 special radiosonde observations	13

7.2.7  Malaysia	13

7.2.8  Indonesia	14

7.2.9  Philippines	14

7.2.10  Hawaii	15

7.3	Research Vessel (R/V)-based Radiosonde Stations	16

7.3.1  R/V Radiosonde Observations as Part of Typhoon Hunter-2008 (TH-08)	16

7.3.2  R/V Radiosonde Observations as Part of PALAU2008	17

7.4	Dropsondes	18

7.4.1  NRL P-3	18

7.4.2  DLR Falcon	19

7.4.3  Air Force WC-130	19

7.4.4  Astra Jet (DOTSTAR)	20

7.4.5  Gulfstream-II (PALAU2008)	21

# Chapter 7.  Sounding Operations

## 7.1	Driftsonde Facility

To be provide by Vidal

## 7.2	Ground-based Radiosonde Stations

This section describes the ground-based sounding stations in the T-PARC region.  For the purposes of this section, the T-PARC region is defined as 0-55 degrees N latitude and 110-160 degrees E longitude.  The information on radiosonde stations within this section is from the Global Telecommunications System (GTS) feed for January-March 2008 (and earlier in some instances) and the World Meteorological Organization (WMO) Publication 9, Volume A, Observing Stations (15 March 2008 edition).  The information on radiosonde type and windfinding methodology is from the WMO Catalogue of Radiosondes and Upper-air Wind Systems (July 2007 edition).  Figure 7.1 provides an overview of the radiosonde locations in the T-PARC region.  The following subsections details on the radiosonde operations by country.

Figure 7.1 Radiosonde locations in the T-PARC region (0-55N and 110-160E).

Real-time data will consist of standard mandatory and significant levels of pressure, temperature, relative humidity, wind speed and wind direction disseminated via the GTS (see Tables 7-1 to 7-10 for details on which stations will transmit in real time).  Note that for inclusion in the forecast models special soundings are only accepted within the period 3 hours before the initialization time and 2.5 hours after the initialization time.  For some stations yet to be determined the high resolution (varying from 1-second to 6-second vertical levels) data will be included in the final T-PARC archive.  The high resolution data have been requested and will be received via ftp.

### 7.2.1  Russia

The Russia radiosonde stations are depicted in Figure 7.2 and Table 7-1.  There are 15 Russian sounding stations in the T-PARC region.  There are 14 stations that provide 00 and 12 UTC TEMP messages on the GTS.  An additional station (Severo-Kuril’sk) has sent TEMP messages on the GTS as recently as July 2007???.  The Russian stations in the T-PARC region all utilize the MRZ radiosonde and secondary radar windfinding technology.

Figure 7.2 Russian radiosonde station locations.

Table 7-1.  Routine radiosonde observations in Russia.  The 00, 06, 12, and 18 columns provide information on UTC release times of radiosondes (R) and pilot balloons (Pi) at the stations.  The GTS column specifies whether observations from the station are routinely available via the GTS.

| Station Name | WMO ID | Lat | Lon | 00 | 06 | 12 | 18 | Sonde Type | Windfinding | GTS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Bagdarin | 30554 | 54.62 | 113.13 | R |  | R |  | MRZ | Secondary Radar | Y |
| Chita | 30758 | 52.02 | 113.33 | R |  | R |  | MRZ | Secondary Radar | Y |
| Borzya | 30965 | 50.38 | 116.52 | R |  | R |  | MRZ | Secondary Radar | Y |
| Zeja | 31300 | 53.75 | 127.23 | R |  | R |  | MRZ | Secondary Radar | Y |
| Nikolaevsk-na-amure | 31369 | 52.15 | 140.70 | R |  | R |  | MRZ | Secondary Radar | Y |
| Blagovescensk | 31510 | 50.27 | 127.50 | R |  | R |  | MRZ | Secondary Radar | Y |
| Sutur | 31538 | 50.07 | 132.13 | R |  | R |  | MRZ | Secondary Radar | Y |
| Habarovsk | 31736 | 48.53 | 135.23 | R |  | R |  | MRZ | Secondary Radar | Y |
| Dal'nerechensk | 31873 | 45.87 | 133.73 | R |  | R |  | MRZ | Secondary Radar | Y |
| Vladivostok | 31977 | 43.27 | 132.05 | R |  | R |  | MRZ | Secondary Radar | Y |
| Aleksandrovsk-sahalinskij | 32061 | 50.90 | 142.17 | R |  | R |  | MRZ | Secondary Radar | Y |
| Poronajsk | 32098 | 49.22 | 143.10 | R |  | R |  | MRZ | Secondary Radar | Y |
| Juzhno-Sahalinsk | 32150 | 46.92 | 142.73 | R |  | R |  | MRZ | Secondary Radar | Y |
| Severo-Kuril’sk | 32215 | 50.68 | 156.13 |  |  |  |  | MRZ | Secondary Radar | N |
| Petropavlovsk-kamchatskij | 32540 | 52.97 | 158.75 | R |  | R |  | MRZ | Secondary Radar | Y |

### 7.2.2  Democratic People's Republic of Korea (North Korea)

The DPRK radiosonde stations are depicted in Figure 7.3 and Table 7-2.  There are two DPRK stations in the T-PARC region.  One station (Pyongyang) provides 00 UTC temp messages on the GTS.  An additional station is mentioned in WMO Publication 9, Volume A, Observing Stations and WMO Catalogue of Radiosondes (July 2007) as releasing radiosondes at 00 and 12 UTC.  This station does not send data to the GTS.

Figure 7.3 DPRK and Republic of Korea radiosonde station locations (left) and pilot balloon station locations (right).

Table 7-2.  Same as Table 7-1 but for the DPRK.

| Station Name | WMO ID | Lat | Lon | 00 | 06 | 12 | 18 | Sonde Type | Windfinding | GTS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Hamheung | 47041 | 39.93 | 127.55 | R |  | R |  |  | Unknown | N |
| Pyongyang | 47058 | 39.03 | 125.78 | R |  |  |  | Poin contacting radiosonde (domestic production) | Hand-operating | Y |

### 7.2.3  Republic of Korea (South Korea)

The Republic of Korea radiosonde and pilot balloon stations are depicted in Figure 7.3 and Table 7-3.  There are seven Republic of Korea radiosonde stations in the T-PARC region.  Two of these stations (Osan and Gwangju) conduct radiosonde releases four times per day and the other five stations conduct twice daily releases.  All of the radiosonde stations except one (Gosan) submit their data to the GTS.  Additionally 9 stations conduct 00 UTC pilot balloon observations and one station (Wonju) conducts 00 and 06 UTC pilot balloon observations.  None of these pilot balloon observations are submitted to the GTS.  South Korea utilizes a mix of radiosonde types with most using the Graw DFM-97 and others using the Jinyang (J/Yang) radiosonde.  GPS or Loran is used for windfinding.

Table 7-3.  Same as Table 7-1 but for the Republic of Korea.

| Station Name | WMO ID | Lat | Lon | 00 | 06 | 12 | 18 | Sonde Type | Windfinding | GTS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Yeoju | 47083 | 37.33 | 127.58 | Pi |  |  |  |  |  | N |
| Maesalli | 47084 | 37.35 | 127.25 | Pi |  |  |  |  |  | N |
| Ungcheon | 47086 | 36.22 | 126.53 | Pi |  |  |  |  |  | N |
| Sokcho | 47090 | 38.25 | 128.57 | R |  | R |  | Graw DFM-97 | GPS/Loran | Y |
| Baengnyeongdo | 47102 | 38.03 | 127.15 | R |  | R |  | Graw DFM-97 | GPS/Loran | Y |
| Gangneung | 47107 | 37.73 | 128.93 | Pi |  |  |  |  |  | N |
| Seoul | 47111 | 37.45 | 127.10 | Pi |  |  |  |  |  | N |
| Wonju | 47118 | 37.42 | 127.95 | Pi | Pi |  |  |  |  | N |
| Suwon | 47120 | 37.22 | 127.00 | Pi |  |  |  |  |  | N |
| Osan | 47122 | 37.10 | 127.03 | R | R | R | R | J/Yang | Loran | Y |
| Pilseung Range | 47123 | 37.10 | 128.87 | Pi |  |  |  |  |  | N |
| Yecheon | 47134 | 36.62 | 128.35 | Pi |  |  |  |  |  | N |
| Pohang | 47138 | 36.03 | 129.38 | R |  | R |  | Graw DFM-97 | GPS/Loran | Y |
| Gwangju | 47158 | 35.12 | 126.82 | R | R | R | R | J/Yang | Loran | Y |
| Sacheon | 47161 | 35.07 | 128.05 | Pi |  |  |  |  |  | N |
| Heuksando | 47169 | 34.68 | 125.45 | R |  | R |  | Graw DFM-97 | GPS/Loran | Y |
| Gosan | 47185 | 33.28 | 126.17 | R |  | R |  | VRS80L | GPS/Loran | N |

#### 7.2.3.1 Enhanced Observations as Part of the Korean Enhanced Observing Period (KEOP)

As part of the Korean Enhanced Observing Period (KEOP) all seven of the Republic of Korea radiosonde stations (see Figure 7.3 and Table 7-3) will be conducting 6-hourly radiosonde releases at 00, 06, 12 and 18 UTC during August and September 2008.  It is unclear whether the enhanced 06 and 18 UTC radiosondes will be transmitted to GTS.

Also, as part of the Sand and dust storm & Aerosol Observational Experiment which is taking place during April and May 2008 there will be radiosonde releases at the GAWC supersite (see Figure 7.3).  It is unclear if these radiosonde observations will continue at this location during August and September 2008.  It is also unclear whether these observations will be sent on the GTS.

### 7.2.4  Japan

The Japan radiosonde and pilot balloon stations are depicted in Figure 7.4 and Table 7-4.

There are 20 stations in Japan that provide 00 and 12 UTC releases on the GTS.  There is one additional station (Iwojima) that sometimes conducts 00 UTC radiosonde releases that are sometimes available on GTS (Iwojima).  Additionally, there is one station (Iwakuni) that conducts twice daily pilot balloon observations and one station (Iejima) that conducts 00 UTC pilot balloons.  Neither of these pilot balloon stations are available on GTS.  Japan typically utilizes one of the varieties of Meisei radiosondes with a couple of stations using Vaisala or VIZ radiosondes.

Table 7-4.  Same as Table 7-1 but for Japan

| Station Name | WMO ID | Lat | Lon | 00 | 06 | 12 | 18 | Sonde Type | Windfinding | GTS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wakkanai | 47401 | 45.42 | 141.68 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Sapporo | 47412 | 43.05 | 141.33 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Nemuro | 47420 | 43.33 | 145.58 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Misawa | 47580 | 40.68 | 141.38 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Akita | 47582 | 39.72 | 140.10 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Sendai | 47590 | 38.27 | 140.90 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Wajima | 47600 | 37.38 | 136.90 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Tateno | 47646 | 36.05 | 140.13 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Hachijojima/Omure | 47678 | 33.12 | 139.78 | R |  | R |  | VRS92 | GPS | Y |
| Hamamatsu | 47681 | 34.73 | 137.67 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Yonago | 47744 | 35.43 | 133.35 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Iwakuni | 47764 | 34.13 | 132.23 | Pi |  | Pi |  |  |  | N |
| Shionomisaki | 47778 | 33.34 | 135.77 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Fukuoka | 47807 | 33.58 | 130.38 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Kagoshima | 47827 | 31.63 | 130.58 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Tokushima | 47881 | 34.13 | 134.60 | R |  |  |  |  |  | N |
| Naze/Funchatoge | 47909 | 28.38 | 129.55 | R |  | R |  | Meisei (RS-016) | GPS | Y |
| Ishigakimima | 47918 | 24.33 | 124.17 | R |  | R |  | Meisei (RS-016) | GPS | Y |
| Naha | 47936 | 26.20 | 127.68 | R |  | R |  | Meisei (Meir91) | Radiotheodolite | Y |
| Iejima | 47938 | 27.72 | 127.78 | Pi |  |  |  |  |  | N |
| Minamidaitojima | 47945 | 25.83 | 131.23 | R |  | R |  | VRS92 | GPS | Y |
| Chichijima | 47971 | 27.08 | 142.18 | R |  | R |  | VIZ II | GPS | Y |
| Iwojima | 47981 | 24.78 | 141.33 | R |  |  |  | Meisei (Meir80) | Radiotheodolite | rare |
| Minamitorishima | 47991 | 24.30 | 153.97 | R |  | R |  | Meisei (RS016) | GPS | Y |

Figure 7.4 Japan radiosonde station locations (left) and pilot balloon station locations (right).  The TH-08 special observation locations are depicted in yellow.

#### 7.2.4.1 Enhanced Observations as Part of Typhoon Hunter-2008 (TH-08)

As part of the Typhoon Hunter-2008 (TH-08) program, Japan will have four 24-hour special observation periods.  During these periods, up to four radiosonde stations will be conducting 3 hourly radiosonde observations.  The four radiosonde stations conducting these observations include Hachijyo-jima (47678), Naze (47909), Minamidaitou-jima (47945), and/or Ishigaki-jima (47918) (see Figure 7.4).  These special observations will be available on the GTS. The JMA Operations Center will make the decision on the declaration of a special observation period in coordination with other groups.

### 7.2.5  China

The China radiosonde and pilot balloon stations are depicted in Figure 7.5 and Table 7-5.

There are 13 stations that conduct 00 and 12 UTC radiosonde releases that send temp messages on the GTS.  An additional 34 stations also conduct 00 and 12 UTC radiosonde releases but only send the mandatory level temp message to the GTS.  All China stations (except Hong Kong) utilize one of the Shanghai Radio (Shang) radiosondes.  “Shang/M" is the old GZZ-2 radiosonde with goldbeaters' skin hygrometer and these stations use the P band radar for windfinding. “Shang/E" is the new GTS-1 radiosonde with a carbon hygristor and these stations utilize the new L band radar for windfinding.

Figure 7.5 China radiosonde station locations that provide only mandatory level data on the GTS (left) and that provide mandatory and significant level data on the GTS (right).

Table 7-5.  Same as Table 7-1 but for China.

| Station Name | WMO ID | Lat | Lon | 00 | 06 | 12 | 18 | Sonde Type | Windfinding | GTS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Hong Kong | 45004 | 22.32 | 114.17 | R |  | R |  | VRS92G | GPS/Loran | Y |
| Hailar | 50527 | 49.22 | 119.75 | R |  | R |  | Shang/M | P-band radar | Y* |
| Nenjiang | 50557 | 49.17 | 125.23 | R |  | R |  | Shang/E | L-band radar | Y* |
| Yichun | 50774 | 47.72 | 128.90 | R |  | R |  | Shang/E | L-band radar | Y* |
| Harbin | 50953 | 45.75 | 126.77 | R |  | R |  | Shang/E | L-band radar | Y* |
| Erenhot | 53068 | 43.65 | 112.00 | R |  | R |  | Shang/E | L-band radar | Y* |
| Hohhot | 53463 | 40.82 | 111.68 | R |  | R |  | Shang/E | L-band radar | Y |
| Taiyuan | 53772 | 37.78 | 112.55 | R |  | R |  | Shang/M | P-band radar | Y |
| Xilin Hot | 54102 | 43.95 | 116.07 | R |  | R |  | Shang/E | L-band radar | Y* |
| Tongliao | 54135 | 43.60 | 122.27 | R |  | R |  | Shang/M | P-band radar | Y* |
| Changchun | 54161 | 43.90 | 125.22 | R |  | R |  | Shang/M | P-band radar | Y* |
| Chifeng | 54218 | 42.27 | 118.97 | R |  | R |  | Shang/M | P-band radar | Y |
| Yanji | 54292 | 42.88 | 129.47 | R |  | R |  | Shang/E | L-band radar | Y* |
| Shenyang | 54342 | 41.77 | 123.43 | R |  | R |  | Shang/E | L-band radar | Y |
| Linjiang | 54374 | 41.72 | 126.92 | R |  | R |  | Shang/M | P-band radar | Y* |
| Beijing | 54511 | 39.93 | 116.28 | R |  | R |  | Shang/E | L-band radar | Y |
| Dalian | 54662 | 38.90 | 121.63 | R |  | R |  | Shang/E | L-band radar | Y* |
| Zhangqiu | 54727 | 36.70 | 117.55 | R |  | R |  | Shang/E | L-band radar | Y |
| Qingdao | 54857 | 36.07 | 120.33 | R |  | R |  | Shang/E | L-band radar | Y* |
| Zhengzhou | 57083 | 34.72 | 113.65 | R |  | R |  | Shang/E | L band radar | Y |
| Nanyang | 57178 | 33.02 | 112.53 | R |  | R |  | Shang/E | L band radar | Y* |
| Yichang | 57461 | 30.70 | 111.28 | R |  | R |  | Shang/E | L band radar | Y* |
| Wuhan | 57494 | 30.62 | 114.13 | R |  | R |  | Shang/M | P band radar | Y |
| Changsha | 57679 | 28.20 | 113.08 | R |  | R |  | Shang/E | L band radar | Y |
| Huaihua | 57749 | 27.57 | 110.00 | R |  | R |  | Shang/M | P band radar | Y* |
| Guilin | 57957 | 25.33 | 110.30 | R |  | R |  | Shang/E | L band radar | Y* |
| Chenzhou | 57972 | 25.83 | 113.02 | R |  | R |  | Shang/E | L band radar | Y* |
| Ganzhou | 57993 | 25.85 | 114.95 | R |  | R |  | Shang/M | P band radar | Y* |
| Xuzhou | 58027 | 34.28 | 117.15 | R |  | R |  | Shang/E | L band radar | Y* |
| Sheyang | 58150 | 33.77 | 120.25 | R |  | R |  | Shang/E | L band radar | Y* |
| Fuyang | 58203 | 32.93 | 115.83 | R |  | R |  | Shang/M | P band radar | Y* |
| Nanjing | 58238 | 32.00 | 118.80 | R |  | R |  | Shang/E | L band radar | Y |
| Shanghai | 58362 | 31.40 | 121.47 | R |  | R |  | Shang/E | L band radar | Y |
| Anqing | 58424 | 30.52 | 117.03 | R |  | R |  | Shang/E | L band radar | Y* |
| Hangzhou | 58457 | 30.23 | 120.17 | R |  | R |  | Shang/E | L band radar | Y* |
| Nanchang | 58606 | 28.60 | 115.92 | R |  | R |  | Shang/E | L band radar | Y* |
| Qu Xian | 58633 | 28.97 | 118.87 | R |  | R |  | Shang/E | L band radar | Y* |
| Hongjia | 58665 | 28.65 | 120.08 | R |  | R |  | Shang/E | L band radar | Y* |
| Shaowu | 58725 | 27.33 | 117.43 | R |  | R |  | Shang/E | L band radar | Y* |
| Fuzhou | 58847 | 26.08 | 119.28 | R |  | R |  | Shang/E | L band radar | Y* |
| Taibei | 58968 | 25.03 | 121.53 | R |  | R |  | Shang/M | P band radar | Y* |
| Xiamen | 59134 | 24.45 | 118.07 | R |  | R |  | Shang/E | L band radar | Y* |
| Wuzhou | 59265 | 23.48 | 111.30 | R |  | R |  | Shang/E | L band radar | Y* |
| Qing Yuan | 59280 | 23.67 | 113.05 | R |  | R |  | Shang/M | P band radar | Y |
| Shantou | 59316 | 23.40 | 116.68 | R |  | R |  | Shang/E | L band radar | Y* |
| Haikou | 59758 | 20.03 | 110.35 | R |  | R |  | Shang/M | P band radar | Y* |
| Xisha Dao | 59981 | 16.83 | 112.33 | R |  | R |  | Shang/E | L band radar | Y* |

* Only mandatory level observations are available on the GTS from these stations.

### 7.2.6  Micronesia, Brunei and Guam

The Micronesia, Brunei, and Guam radiosonde and pilot balloon stations are depicted in Figure 7.6 and Table 7-6.  There are six stations that conduct 00 and 12 UTC releases and send temp messages on the GTS.  One of these stations also conducts 06 and 18 UTC pilot balloon releases that do not get sent on GTS.  Five of the stations (all except Brunei) have their high vertical resolution (6-second) data routinely archived at NCAR/EOL.  These high resolution data are typically available with a two month delay.

Figure 7.6 Radiosonde (top) and pilot balloon (bottom) station locations in Micronesia, Malaysia, Indonesia, Philippines, and Brunei Darussalam.

Table 7-6.  Same as Table 7-1 but for sites in Micronesia and Brunei Darussalam.

| Station Name | WMO ID | Lat | Lon | 00 | 06 | 12 | 18 | Sonde Type | Windfinding | GTS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Guam | 91212 | 13.55 | 144.83 | R |  | R |  | VIZ B2 | Radiotheodolite | Y* |
| Woleai Atoll | 91317 |  |  |  |  |  |  | VRS92 |  | N |
| Chuuk | 91334 | 7.47 | 151.85 | R |  | R |  | VRS80-57H | Radiotheodolite | Y* |
| Pohnpei | 91348 | 6.97 | 158.22 | R |  | R |  | VRS80-57H | Radiotheodolite | Y* |
| Koror | 91408 | 7.33 | 134.48 | R |  | R |  | VRS80-57H | Radiotheodolite | Y* |
| Yap | 91413 | 9.48 | 138.08 | R |  | R |  | VRS80-57H | Radiotheodolite | Y* |
| Brunei | 96315 | 4.93 | 114.93 | R | Pi | R | Pi | VRS92G | GPS | Y** |

* High vertical resolution (6 second) data for these stations are routinely collected by                    NCAR/EOL.

** Only the radiosonde data at 00 and 12 UTC are available on GTS.

#### 7.2.6.1  PALAU2008 special radiosonde observations

As part of PALAU2008, Yap (91413) and Koror (91408) will be conducting additional radiosonde releases at 06 and 18 UTC during the period from 5 June to 15 July 2008.  TEMP messages for these special observations will also be sent to the GTS.  Additionally, special radiosonde releases will be conducted at Woleai atoll (91317; see Figure 7.6 and Table 7-6) from 5 June to 15 July 2008.  These will be either 12- or 6-hourly observations.  These observations are not currently planned to be available on the GTS.

### 7.2.7  Malaysia

The Malaysia radiosonde and pilot balloon stations are depicted in Figure 7.6 and Table 7-7.  There are four stations that conduct 00 and 12 UTC releases and send temp messages on the GTS.  Three of these stations also conduct 06 and 18 UTC pilot balloon observations that are not available on GTS.  Additionally, one station conducts 00, 06, 12 and 18 UTC pilot balloon observations that are not available on GTS.

Table 7-7.  Same as Table 7-1 but for Malaysia.

| Station Name | WMO ID | Lat | Lon | 00 | 06 | 12 | 18 | Sonde Type | Windfinding | GTS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Kuching | 96413 | 1.48 | 110.33 | R | Pi | R | Pi | VRS92G | GPS | Y* |
| Bintulu | 96441 | 3.20 | 113.03 | R | Pi | R | Pi | VRS92G | GPS | Y* |
| Kota Kinabalu | 96471 | 5.93 | 116.05 | R | Pi | R | Pi | VRS92G | GPS | Y* |
| Tawau | 96481 | 4.27 | 117.88 | R |  | R |  | VRS92G | GPS | Y |
| Sandakan | 96491 | 5.90 | 118.07 | Pi | Pi | Pi | Pi |  |  | N |

* Only the radiosonde data at 00 and 12 UTC are available on GTS.

### 7.2.8  Indonesia

The Indonesia radiosonde and pilot balloon stations are depicted in Figure 7.6 and Table 7-8.  There is one station that conducts 00 and 12 UTC releases and sends temp messages on the GTS.  This station also conducts 06 and 18 UTC pilot balloon observations that are not available on GTS.  Seven additional stations conduct pilot balloon observations (three at 00, 06 and 12 UTC; three at 00 and 12 UTC; and 2 at 00 UTC) that are not available on the GTS.

Table 7-8.  Same as Table 7-1 but for Indonesia.

| Station Name | WMO ID | Lat | Lon | 00 | 06 | 12 | 18 | Sonde Type | Windfinding | GTS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Tarakan/Juwata | 96509 | 3.33 | 117.57 | Pi |  | Pi |  |  |  | N |
| Tanjung Redep/Kalimarau | 96529 | 2.12 | 117.45 | Pi |  |  |  |  |  | N |
| Putussibau/Pagsuma | 96565 | 0.88 | 112.93 | Pi |  |  |  |  |  | N |
| Naha/Tahuna | 97008 | 3.58 | 125.47 | Pi |  | Pi |  |  |  | N |
| Menado | 97014 | 1.53 | 124.92 | R | Pi | R | Pi | VIZB | Radiotheodolite | Y* |
| Toli-Toli/Lalos | 97028 | 1.02 | 120.8 | Pi | Pi | Pi |  |  |  | N |
| Gorontalo/Jalaluddin | 97048 | 0.52 | 123.07 | Pi |  | Pi |  |  |  | N |
| Ternate/Babullah | 97430 | 0.77 | 127.37 | Pi | Pi | Pi |  |  |  | N |

* Only the radiosonde data at 00 and 12 UTC are available on GTS.

### 7.2.9  Philippines

The Philippines radiosonde and pilot balloon stations are depicted in Figure 7.6 and Table 7-9.  None of the Philippines stations have appeared on the GTS since Nov/Dec 2007.  There are four stations that conduct 00 UTC radiosonde releases, five stations that conduct 00 and 12 UTC pilot balloon observations and one station that conducts 00 and 06 UTC pilot balloon observations.

Table 7-9.  Same as Table 7-1 but for the Philippines.

| Station Name | WMO ID | Lat | Lon | 00 | 06 | 12 | 18 | Sonde Type | Windfinding | GTS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Basco | 98135 | 20.45 | 121.97 | Pi |  | Pi |  |  |  | N |
| Laoag | 98223 | 18.18 | 120.53 | R |  |  |  | Graw DFM-90 | GPS | N* |
| Baguio | 98223 | 16.42 | 120.6 | Pi |  | Pi |  |  |  | N |
| Tanay | 98433 | 14.57 | 121.37 | R |  |  |  | VIZ GPS Mark II | GPS | N* |
| Legaspi | 98444 | 13.13 | 123.73 | R |  |  |  | VRS92G | GPS | N* |
| Cuyo | 98630 | 10.85 | 121.03 | Pi | Pi |  |  |  |  | N |
| Mactan | 98646 | 10.3 | 123.97 | R |  |  |  | VRS92G | GPS | N* |
| Surigao | 98653 | 9.8 | 125.5 | Pi |  | Pi |  |  |  | N |
| Davao | 98753 | 7.12 | 125.65 | Pi |  | Pi |  |  |  | N |
| Zamboanga | 98836 | 6.90 | 122.07 | Pi |  | Pi |  |  |  | N |

* These sites last routinely appeared on the GTS in Nov/Dec 2007.  Tanay started to occasionally appear on GTS again 22 April 2008.

### 7.2.10  Hawaii

To support the driftsonde operations the radiosonde data from Hawaii will also be available.  The Hawaiian radiosonde stations are described in Table 7-10.  All stations are routinely available in real-time on GTS.  NCAR/EOL routinely archives the high resolution (6-second) data from these stations.  The high resolution data are typically available on about a two month delay.

Table 7-10.  Same as Table 7-1 but for Hawaii.

| Station Name | WMO ID | Lat | Lon | 00 | 06 | 12 | 18 | Sonde Type | Windfinding | GTS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lihue | 91165 | 22.00 | 159.40 | R |  | R |  | VRS80-57H | Radiotheodolite | Y |
| Hilo | 91285 | 19.70 | 155.10 | R |  | R |  | VIZ B2 | Radiotheodolite | Y |

## 7.3	Research Vessel (R/V)-based Radiosonde Stations

This section covers the special Research Vessel soundings operations that are occurring during T-PARC.  These include three ships as part of the TH-08 experiment and one as part of the PALAU2008 experiment.  Details on operations are in the following subsections.

Note that for inclusion in the forecast models special soundings are only accepted within the period 3 hours before the initialization time and 2.5 hours after the initialization time.

### 7.3.1  R/V Radiosonde Observations as Part of Typhoon Hunter-2008 (TH-08)

Japan will have three Research Vessels (R/V) taking part in TH-08 with a maximum of two taking part at any one time.  Table 7-11 summarizes the R/V participation in TH-08 and Figure 7.7 shows the location of the ships.  When each R/V is on station it will be conducting 12 hourly (00 and 12 UTC) radiosonde releases.  When a TH-08 Special Observation period has been called, one or both of the R/V’s on station at that time will conduct radiosonde releases every three hours for a 24 hour period.  There will be at most four Special Observation periods as part of TH-08 during August and September 2008.  All ships will send TEMP messages to the GTS.

Table 7-11.  R/V radiosonde observations for TH-08

| R/V Name | WMO ID | Lat | Lon | Time Period | Sonde Type | Windfinding | GTS |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Ryofu-maru | JGQH | 28.00 | 132.00 | Early-late August |  |  | Y |
| Seifu-maru | JIVB | 32.00 | 127.00 | Early-late September |  |  | Y |
| Chofu-maru | JCCX | 32.00 | 127.00 | Mid-late August |  |  | Y |
| Chofu-maru | JCCX | 28.00 | 137.00 | Early-mid September |  |  | Y |

Figure 7.7 TH-08 Research Vessel radiosonde locations.

### 7.3.2  R/V Radiosonde Observations as Part of PALAU2008

During June and July 2008 the Japanese R/V Mirai will be releasing radiosondes every 6 hours.  For the period from 4-28 June 2008 the R/V Mirai will be on station at 12N and 135E.  From 30 June to 3 July the R/V Mirai will be in port at Guam (no radiosondes during this period).  Following this, from 4-27 July 2008, the R/V Mirai will be conducting a cruise to replace Triton buoys.  Table 7-12 summarizes the R/V Mirai radiosonde observations and Figure 7.8 shows the location of the ship.  TEMP messages will be sent to the GTS via JMA.

Table 7-12.  R/V radiosonde observations for PALAU2008

| R/V Name | WMO ID | Lat | Lon | Time Period | Sonde Type | Windfinding | GTS |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Mirai | JNSR | 12.00 | 135.00 | 4-28 June | VRS92 |  | Y |
| Mirai | JNSR | Moving (see Figure 7.8) | 4-28 July | VRS92 |  | Y |

Figure 7.8 PALAU2008 R/V Mirai cruise map.

## 7.4	Dropsondes

Note that for inclusion in the forecast models special soundings are only accepted within the period 3 hours before the initialization time and 2.5 hours after the initialization time.

### 7.4.1  NRL P-3

The NRL P-3 will be based in Guam from 30 July to 30 September 2008.  The NRL-P3 has a total of 150 research flight hours and a total of 350 Vaisala RD93 dropsondes (~30 dropsondes per flight) which use GPS for windfinding.  The high resolution (0.5 second) “D” file will be transmitted to the Monterey Operations Center via LDM.  Once in Monterey, the file will be processed through the NCAR/EOL ASPEN sounding processing software, which removes outliers and noise, and examined before a TEMP message is generated, which will be transmitted to the GTS probably via email through an NCAR/EOL arrangement with the NWS. The “D” file format is shown in Figure 7.9.

Figure 7.9 Example of the “D” file format.

If the P-3 flies at 24,000ft, the high resolution data files are about 100kb.  The NRL P-3 will typically release dropsondes at 60nmi intervals and at waypoints (section 3.3.b??).

### 7.4.2  DLR Falcon

The DLR Falcon will be based in Atsugi, Japan from 25 August to 4 October 2008.  The DLR Falcon will have 300 dropsondes from NSF and an additional 37 dropsondes from JMA as a part of the TH-08 experiment.  The DLR Falcon will be utilizing Vaisala RD93 dropsondes which use GPS for windfinding.  The DLR Falcon has a desired flight level of 270 to 370.  Every other dropsonde will have a TEMP message transmitted to the GTS in real-time.  The methodology of transmission is still under discussion.  The high resolution “D” file data are 0.5 second resolution and contain pressure, temperature, relative humidity, wind speed and wind direction.

During single aircraft operations, the DLR Falcon will release dropsondes at 8-10 minute intervals (100-125km spacing) in conditions sub-optimal for the lidar and possibly at higher frequency during optimal lidar conditions (see section 3.3.a??).  A typical mission will include two flights for a total of 6-7 hours.

During multiple aircraft operations (section 3.3.b??) the DLR Falcon will release dropsondes at about 10 minute intervals (~125 km spacing) or about 15-20 dropsondes per flight.  As with the single aircraft operations a mission could include two flights with a refueling in between.

### 7.4.3  Air Force WC-130

The Air Force WC-130 will be based in Guam from 30 July to 30 September 2008.  This aircraft will have approximately 750 dropsondes.  The Air Force will process the data through the ASPEN software and send the TEMP message data to the NHC Chief, Aerial Reconnaissance Coordination, All Hurricanes (CARCAH) unit via satellite down link.  Once at CARCAH, the data are quality controlled and transmitted to the GTS.  The high resolution (0.5 second) “D” file data will be available after the plane lands.

The WC-130 aircraft will typically fly at ~10,000ft with a maximum altitude of 20,000ft (see section 3.3.b??).  Dropsondes will be released regardless of altitude as closely as possible.  From 10,000ft, dropsondes can be released as frequently as every 2.5 minutes (~18 km spacing).  Higher resolution is always possible for a burst of four dropsondes.

### 7.4.4  Astra Jet (DOTSTAR)

The Astra Jet will be based in Taiwan and flights will be primarily in the area south and east of Taiwan (see Figure 7.10).  The Astra Jet will be utilizing Vaisala RD-93 dropsondes.  This aircraft will have approximately 150 dropsondes.  There will be eight missions each 6 hours in length.  Approximately 15 dropsondes will be released each flight.  See Figure 7.10 for an example flight strategy.

Figure 7.10 Example dropsonde release strategy for the DOTSTAR aircraft.

The dropsonde data will be sent in real time from the aircraft to the Central Weather Bureau via sitcom.  The CWB will insert TEMP messages onto the GTS (Figure 7.11).

Figure 7.11 DOTSTAR dropsonde data flow and areal coverage.

### 7.4.5  Gulfstream-II (PALAU2008)

During June 2008 a Gulfstream-II aircraft will release dropsondes in the Palau Island region.  There will be 3-4 flight days.