## Slide 1: GV Flight Level Data
Cory Wolff
ORCAS Science Meeting
7 September 2016

## Slide 2: Summary
Release of LR data
  Coming soon
Overall, good data quality
Some minor, recurring issues
Topics
  Fast response temperature
  Dew points
  King probe
  Missing flights
  CN counter
  Winds

## Slide 3
Fast response temperature
  Some icing problems
King probe
  Showed cloud at start of each flight before correcting
  Looking into this, data removed

## Slide 4
Dew points
  Mirror instruments have known issues
    Can’t hit low dew points
    Oscillations
    Flooding on descents
  DPL missing until RF04

## Slide 5
Flights with no data
  Timeserver sync issue
  All of RF12; half of RF13 (evacuation and return)
Winds
  Drift in WIC
  Ongoing issue
  Apply corrections based on altitude
CN Counter
  I/O card failure
    Missing RF02 - RF06
  Becomes increasingly inefficient above 300 mb (~9 km) and undercounts particles
    Effect is size dependent and can’t be corrected for

## Slide 6: Questions?