## Slide 1: Daily schedule strawman plan
Kiruna time: CET
UTC + 1 till 3/30/’24
UTC + 2 from 3/31
Factors:
  For F1/F2 flights, prefer to be at the Arctic ice edge during daylight hours
24°E
Kiruna
.
2 hourly radiosondes from Bear Island & Jan Mayen
Bear
Island
Jan
Mayen

## Slide 2
LON | UTC | CET
10°W | 12:40 | 13:40
0 | 12:00 | 13:00
10°E | 11:20 | 12:20
20°E | 10:40 | 11:40
24°E | 10:24 | 11:24
time of local solar noon
CAESAR
starts
CAESAR
ends
Maybe the earliest flights in the campaign (Feb) should not target the Arctic ice edge

## Slide 3: Daily schedule – strawman plan
Kiruna time: CET
UTC + 1 till 3/30/’24
UTC + 2 from 3/31
Factors:
  For F1/F2 flights, prefer to be at the Arctic ice edge during daylight hours
  C130 crew duty limitations
    max # consecutive work days before hard down day: 6
    max “work” hrs/day: 14
    min crew rest period (“non-work”): 12
    max # flights in row: 2, for full flights (9 hrs) Day 2 to start 2 hrs later than Day 1 (Day 3 would be a short flight)
  back to back flights require 2 flight plans, Day 1 and Day 2
  Met Norway’s preferred forecast time: 5 pm. They can do 2-3 pm as well (crew rotation 4 pm)

## Slide 4: Daily schedule – strawman plan
Kiruna time: CET
UTC + 1 till 3/30/’24
UTC + 2 from 3/31
Typical daily ops:
  Take-off (TO) – 4 hrs: weather update
  TO – 3.5 hrs: relay any flight plan mods to pilots
  TO – 2 hrs? final go/no-go decision
  TO: between 6-8 am CET (5-7 UTC)
  return to ESNQ: 3-5 pm CET (14-16 UTC)
  Land + 0.5 hrs: debrief
  Daily weather briefing: starts 1 pm (12 UTC)
    available products:
      ECMWF 00 Z forecasts, AA 09 Z forecasts, radar and satellite imagery up to 12 Z
    next-day forecast, consider Kiruna terminal wx conditions as well
    back-to-back and longer-term mission planning
  decision for next day ops by 3 pm (14 UTC) so pilot can file flight plan no later than 4 pm
  First possible flight date is 3/9. Start of Dry run: 3/8 at 12 UTC.
  Flight times typically are in the window 5-16 UTC. LSN up north ranges from 10:30 Z (east end) to 12:30 UTC (western Fram Strait)

## Slide 5: Climatological airport weather conditions during CAOs over the Norwegian Sea between 22 Feb – 7 April. Bad conditions for T/O are in red. Bad conditions for T/O and landing in purple
 | Kiruna (ESNQ) | 
 | 1991-2016 | 2017-2022
mean min temperature (C) | -13.4 | -12.5
mean max temperature (C) | -4.3 | -3.9
dry (% of time) | 87.5 | 85.5
rain and drizzle (% of time) | 0.4 | 0.1
snow and mixed precip (% of time) | 12.1 | 14.4
prevailing wind direction (degree) | 200-240 | 200-240
wind speed >20 kts (% of time) | 1.9 | 4.0
cross-track wind speed > 25 kts 1 (% of time) | N/A | 0.4
visibility > 3 miles (% of time) | 92.5 | 86.8
ceiling > 1500 ft (% of time) | 86.2 | 74.2
visibility and/or ceiling too low for VMC 1 | 17.5 | 36.7
VIS/Ceiling too low for VMC and/or snowfall 2 | 28.2 | 45.5
1: IMC ops possible otherwise. Kiruna (ESNQ) has climb gradients in place during IMC conditions, which will reduce the C-130 flight time by 2 hours (maximum weight reduced by 10,000 lbs during IMC). VMC conditions are: ceiling at least 1500 ft and visibility at least 3 statute miles.
2: conditions needed for T/O, since the aircraft with instruments cannot be de-iced

## Slide 6: questions to consider for the Dry Run
Single-day vs back-to-back flights
How do we decide a polar low can be targeted?
Scorecard for hypothesis checking
What flight planning info to provide the Mission Coordinator
Gunnar Noer’s forecast package?

## Slide 7: How to fly F1-F2 long legs with cloud penetrations
Sawtooth legs:
  climb and descend to PI specifications (~500 ft MSL to ~1500 ft above cloud top) and use the clock to ascertain climb and descent points
  Descend/climb at 1,000 FPM
  Note: aircraft can’t go from level to 1,000 climb/descent instantaneously
Flux legs at 500 ft:
  Descent to 500ft requires momentary level off at 1,000ft to calibrate altimeters
  maintain 500 ft for 10 min
in-cloud legs
  maintain for 10 min if icing conditions allow
1000 ft above cloud top legs
  maintain for 10 min

## Slide 8: Pre-flight info the Mission Coordinator (pilots) need from us: Flight plan
F1-F2:
  Terminal target Coordinates – Degrees and Minutes, e.g., N8015 E01015
  preferred initial point waypoint for “research”, i.e. southernmost location with CAO conditions
L, P, S, C:
  starting point and tentative pattern
  refinement possible during outbound ferry
PL
  initial waypoint to ferry to
  refinement of rosette pattern during outbound ferry

## Slide 9: real-time info critical for mission coordination
Real-time satellite/model data to be uploaded to the plane
  MODIS/VIIRS imagery
  AA model output at SL, 900, 800, 700 mb
Real-time CT height (WCR), cloud LWC near cloud top below (WCL/Marli), and cloud base height (dropsondes). This info will be collected on the outbound leg and will inform the inbound leg of F1 flights

## Slide 10
Kiruna
ESNQ
Climatological airport weather conditions during CAESAR:
wind