01/13/09

Maintenance day in Anchorage

The ARINC problem from RF03 appears to have been software. The ARINC came up fine today. Greg said that the DSM status page had red on the ARINC inputs on the flight.

On the DSM status page both IRS’s, the IRIG-B, ADC and the GPS was red.  The rest of the information was working.  I’m guessing that it was some form of a software lockup.

The Red on IRIG-B was just on the first column the rest (NOPPS) did not show up.

I think it might have been some form of CPU lock-up with the IRIG-B also having problems. We have not seen this before but it can bed quickly fixed by a reboot.

The MPDBS DSM can be rebooted individually by the breaker on the Main Power Panel.

Packed the plane for the trip south.  The 4 large flask boxes sit 2X2 and the small flask boxes sit 2X2 next to them.  There looks like there will be enough room but we will have to see tomorrow when all the luggage shows up.