## Slide 1
Chemistry reaction chamber
Pump
Laptop
Heater circuit 1 to anti-ice HIMIL
Power(1): 5.5A/28VDC
Power(2): 4A/110VAC
Power(3): 0.5A/110VAC
Power(4): 8A/28VDC
Ethernet
HIMIL 6A/28VDC
Controller cable(7)
Heater circuit 2 to tube heaters
HIMIL copper sample tube, 4x MINCO heaters,
4x 28VDC/15W
Power(5): 4.5A/28VDC
ELECTRICAL INTERCONNECT DIAGRAM for “New chemistry sensor” IDEAS-4 C-130 project, 08/22/2011 Show all interconnecting cables, circuit protection devices, etc. Template only!
Wire specifications (see www.eol.ucar.edu/instrumentation/aircraft/G-V/documentation/approved-wire)
Wire NCAR-ID
Power(1) STT-16 16-TE-1929(3) STJ
Power(2) STT-16 16-TE-1929(3) STJ
Power(3) STT-16 16-TE-1929(3) STJ
Power(4) STT-16 16-TE-1929(3) STJ
Power(5) STT-16 16-TE-1929(3) STJ
Ethernet E50824 6753
HIMIL heater etc.
Tube wire STP 18-TE-1930(2)STJ 81173
Tube heater Minco HR66xxRxx.xL36B
RS-232 cable etc.
Controller cable STP-22 CME4-02-STW-2219 75859
Maximum power draw
Diagram provided by: Douglas Bogus, db@gmail.com, 303-444-4444
RS-232 to C-130 data system
7A
6A
2A
10A
6A

## Slide 2
Chemistry reaction chamber
Pump
Laptop
Heater circuit 1 to anti-ice HIMIL
Heater circuit 2 to tube heaters
PLUMBING INTERCONNECT DIAGRAM for “New chemistry sensor” IDEAS-4 C-130 project, 08/22/2011 Template only; show all tubing, etc.
Tube specifications (see www.eol.ucar.edu/instrumentation/aircraft/G-V/documentation/approved-wire)
Tube Manufacturer Material Part NCAR-ID
Sample tube Cambridge-Lee ¼”Copper ¼”OD, 0.190”ID
Pump tube Saint-Gobain 3/8”Comp SYNFLEX 1300-06603 677F-6C
Exhaust tube Saint-Gobain 3/8”Comp SYNFLEX 1300-06603 677F-6C
HIMIL anti-iced inlet.
One forward facing ¼”OD SS tube.
Sample tube
Pump tube
Exhaust tube to floor dump
Diagram provided by: Douglas Bogus, db@gmail.com, 303-444-4444.