## Slide 1: Flux Profiles at Intermittent Eddy Development; What The Flux?
A Saga in Two Parts
David Reed
Yohannes G/Eyesus Getahun
Steve Oncley
Tom Horst

## Slide 2: Site Description
Marshall site is located at (39°56' 56.93'' N , 105°11’47.52'' W), elevation 1744 m asl (5722 ft asl).

## Slide 3: Instrumentation
A 10 m high flux tower
Five CSAT3 sonic annemometers installed at five levles (2, 4, 6, 8 and 10 m),
Two LI7500 infrared gas analyzers (IRGA) (4 and 10 m) .
Four component radiation.

## Slide 4: Weather and Atmospheric Stability Conditions
Wave clouds were observed over the Boulder area in the morning, with increasing mid-level clouds during the day.
Haze dominated the area around Boulder and the Marshall site until late afternoon when a thunderstorm with lots of lightning and occasionally heavy rain passed over (Brown and Gary, NCAR Wiki, June 6, 2009)

## Slide 5: Weather and Atmospheric (…)
Vertical profiles produced from the radiosonde ascents indicate nearly neutral or close to adiabatic conditions prevailed in the lowest 1 km (760 mb) capped by inversion or isothermal layers aloft up to 2.5 km (740 mb)

## Slide 6: A Motivating Question Part One
Compare how the heat fluxes affect the energy budget
Changing the averaging times to help close the energy budget
↓sw + ↓lw + ↑sw + ↑lw = Net Rad
Net Rad + Soil Heat Flux = Sensible + Latent Heat Flux
Hopefully?

## Slide 7: Time Series Analysis
Measurements at a fixed point over a period of time
Time series data is widely used
Easy to visualize what is happening
(But yet my advisor says I can’t publish with just time series)

## Slide 8: Frequency Analysis
Fourier Transform to frequency domain
Power of signal at each frequency
-5/3 line is empirical formula of turbulence (Kolmogorov’s Spectrum)

## Slide 9: Frequency Analysis
Cospectra
In phase components of the covariance
Visualize what frequencies are contributing to the flux

## Slide 10: Frequency Axis
Ogive Plot
Cumulative Summation of Cospectra from high frequency to low
Can be used to find frequency at which you can efficiently average and not lose data

## Slide 11: Calculating Averaging Times
Mid day
Developed BL
Very similar to full day Ogive
Averaging time of an hour is plenty fine

## Slide 12: Calculating Averaging Times
Night Time
Stable Atmosphere
Averaging time of less then a minute, or 20, or maybe even 2 hours (In this case study)
2 minute averaging time in general
4am to 6am

## Slide 13: Calculating Averaging Times
Sunrise, BL birth
Increasing fluxes and increasing energy budget imbalance
Averaging time of less then a minute in this case
6am to 8am

## Slide 14: A Closer Look at Boundary Layer Birth
If two minute average times is needed in the early morning, we can look at two minute sections and they should show a leveling off
Or, it’s just a mess

## Slide 15: A Closer Look at Boundary Layer Birth
First 60 minutes
Periods of ‘normal’ two minute sections broken up by smaller scale turbulence

## Slide 16: A Closer Look at Boundary Layer Birth

## Slide 17: Energy Budget on Differential Averaging Time Scales
Five Minute Scale
Captures most flux carrying frequencies, but oversamples during the day time while slightly under-sampling at night/evening/dawn

## Slide 18: Energy Budget on Differential Averaging Time Scales
Thirty Minute Scale
Captures almost all flux carrying frequencies during the day, missing flux at night
Ameriflux standard

## Slide 19: Energy Budget on Differential Averaging Time Scales
Sixty Minute Scale
Captures enough flux carrying frequencies during the day, hopeless at night

## Slide 20: Energy Budget on Differential Averaging Time Scales Results
Five Minute Scale
Mean Energy Budget Imbalance was 72 W/m2
Thirty Minute Scale
Mean Energy Budget Imbalance was 62 W/m2
Sixty Minute Scale
Mean Energy Budget Imbalance was 60 W/m2
There was a difference!

## Slide 21: Energy Budget on Differential Averaging Time Scales Results
What does this mean? I got lucky.
Longer time average was better during the mid-day, but missing flux carrying frequencies at night and during periods of intermittent flux
But most of the flux signal is during the mid-day
Proper use of this could allow dynamic averaging time to match dynamic flux periods

## Slide 22: Research Question
How best to quantify the total flux contributions from eddies that popup and die during intermittent turbulent activities.

## Slide 23: Justification
Energy closure will not be observed, because intermittent fluxes do not satisfy the stationarity condition, and also advection could play a role (Aubinet, 2008; Finnigan et al, 2003).
Measurement of advection requires site-specific experimental setup (Aubinet, 2008).
Decreasing the sampling rate of fluxes increases the uncertainty in the flux estimates, but not the total value of flux estimates (Bosveld and Beljaars, 2001).

## Slide 24: Data
Raw wind and sonic temperature data for June 5, 2009 were used for this case study.

## Slide 25: Methods
Coordinate rotation to streamline coordinates
  The x-axis is aligned with the average direction of the horizontal wind in streamline coordinates(uave),
  Perturbations in the y-direction (vs’) are minimum,
  Average vertical wind sums up to zero (wave =0).
us’= u’cos(θave) + v’sin(θave) (1)
cos(θave) = uave/((uave)2 +(vave)2)½ (2)
sin(θave) = vave/((uave)2 +(vave)2)½ (3)

## Slide 26: Methods (…)
Vertical Momentum Flux (<w’us’> )
<w’us’> = <usw><us><w> (4)
  us Horizontal wind in streamline coordinates.
Heat Flux (<w’ts’>)
<w’ts’> = <wts> (5)
Plots
  Time series and ogive plots were produced.

## Slide 27: Wind and Friction Velocity

## Slide 28: Momentum Flux (w’u’) at Marshall (June 5, 2009)

## Slide 29: Cospectra: Momentum Flux at Marshall (June 5, 2009; 00 – 08 MDT)

## Slide 30: Ogive Plot: Momentum Flux at Marshall (June 5, 2009; 00 – 08 MDT)

## Slide 31: Cospectra: Heat Flux at Marshall (June 5, 2009; 00 – 08 MDT)

## Slide 32: Ogive plot: Heat Flux at Marshall (June 5, 2009; 00 – 08 MDT)

## Slide 33: Conclusions (Yohannes)
Intermittent turbulent fluxes are short lived (~ 1 min), but averaging at longer time periods will eliminate their contribution.
Coordinate transformation alone does not solve the problem of under-representation of the momentum flux from intermittent turbulent fluxes .

## Slide 34: Questions?
Thank you ASP/NCAR
Go Red Wings