RF10

TECH: Cowan

1/28/09

Easter Island to Costa Rica

Pre-flight – VCSEL not working.

Noticed that the tip of the RICE probe is getting black.  Let Kurt Know.

1723 Block out

1725 Takeoff

1726 saw a spike on VCSEL during takeoff, still no data.  Might be an alignment issue.

1751 RICE probe quit reporting for a short time.

1822 At altitude Power reading:

Left Side A Bus

400 Hz Phase A 14.6 A (1A Jump) 116 V

400 Hz Phase B 12.3 (1A Jump) 117 V

400 Hz Phase C 14.5 (1A Jump) 115 V

400 Hz AI Phase A 0A

400 Hz AI Phase B 0A

400 Hz AI Phase C 0A

60 Hz 116V 20A

Right Side B Bus

400 Hz Phase A 8.6 (1A Jump) 115V

400 Hz Phase B 10.9 (1A Jump) 113V

400 Hz Phase C 8.1 (1A Jump) 115V

400 Hz AI Phase A 0A

400 Hz AI Phase B 4.0A 113V

400 Hz AI Phase C 0A

60 Hz 115V 12A

28V AI 28.9V 13A

1848 Rice at a lower value, about .4 to .65 instead of .8

1909 DPL service Mirror on, resetting.

1916 Red light on sever in back, it has an information icon under it.  On the front LCD display says IB110 SBE log disabled.  Found out this is a memory error log that has been disabled due to to many messages.

1950 DPL service Mirror on, resetting.

2006 Left DSM stopped, restarted from switch on ADS sation.

2115 DPL service Mirror on, resetting.

2156 DPL service Mirror on, resetting.

2200 Both Dew Points have Service Mirror, resetting both Dew Point sensors.

2247 DPR service Mirror on, resetting.

2326 DPR service Mirror on, resetting.

2330 DPR service Mirror on, resetting. Looks like DPLS is stuck with a rebalance light on and oscillating.

2333 DPR working resetting DPL to get it out of Rebalance.

0000 Powering off camera DSM

0014 Cycle Power to RW Camera, which is the AI power to that wing. Outboard location only.

0050 Camera issue turned out to be the cable to the DSM from the wing.  Needed to be reset. Also it is hanging down which might be an issue as well. When cable was reset the DSM functioned okay.

0122 Landing

On landing DPR Service Mirror light on, turned it off.  DPL on until parked.

0127 Block in