RF11

TECH:  G.B.

5/14/08

Takeoff 17:05

17:28 – Turned on Himil Heat – forgot on taxi

18:23 – Cycled power on Camera DSM at request of ground

19:10 – Spike in PLWC – Clear air – 50w

20:33 – Spike in PLWC – Clear air – 70w

20:44 – Spike in PLWC – Clear air – 50w

20:57 – Spike in PLWC – Clear air – 70w

21:23 – Spike in PLWC – Clear air – 60w

21:54 – PLWC up to 48w – Level Shift

22:04 – Cycled Left wing anti-ice – no change

22:19 – Cycled Left wing DSM at request of ground

22:20 – Left wing DSM back up and PLWC is again functional

Landing 23:19

ADS locked up on landing.

Everything else worked well.

Notes on PLWC –

- PLWC baseline between 8w -12w in clear air.  Varies with air speed

- 17:28 -  Response in cloud

- 18:17 – 18:24 – Response in cloud

- 18:33 - Spike but believe to be a response to cloud